## Slide 1: ICS 51 Study Guide
By Jean-Paul Nguyen

## Slide 2: I. Structured Computer Organization

## Slide 3: Languages
Machine Language – the language for instructions in programs
General Architecture – large, complex components that allow for multiple programs
• this is too complicated to write in just machine code alone!
• people want to do X, but computers want to do Y

## Slide 4: Levels
The main way to fix this is to create a new, higher-level language that’s easier to use. Machine Level Language is level 0, and the other language is level 1.
However, since the machine computer only does instructions in L0, there are two ways to deal with this:
Translation – take a file of L1 instructions and convert to L0
Interpretation – in runtime, translate incoming L1 instructions to L0

## Slide 5: Virtual Machines
We can now imagine a hypothetical virtual machine that has a higher-level language as its machine language. This now allows us to write programs for that virtual machine in that language, which is then translated or interpreted into the lower-level machine language:
Layer 1
Language: L1
Machine: M1
Layer 0
Language: L0
Machine: M0
Interpret Translate

## Slide 6: Multilevel Machines
We can now make a machine that has multiple levels of translation/interpretation, with the bottom level being the simplest and the top level being the most sophisticated.
For a machine with n levels, we can imagine n virtual machines:
Layer 1
Language: L1
Machine: M1
Layer 0
Language: L0
Machine: M0
Interpret Translate
Layer n
Language: Ln
Machine: Mn
Interpret Translate
Interpret Translate
...

## Slide 7: Contemporary Multilevel Machines
Problem-Oriented Language Level
Assembly Language Level
Operating System Machine Level
Instruction Set Architecture Level
Microarchitecture Level
Digital Logic Level
Level 5
Level 4
Level 3
Level 2
Level 1
Level 0
Translation (compiler)
Translation (assembler)
Partial Interpretation (operating system)
Interpretation (microprogram) / Direct Execution
Hardware
manages computer’s resources
holds instructions to use with data
holds the data like variables
contains the logic to build hardware i.e. boolean gates

## Slide 8: II. Computer Systems

## Slide 9: CPU Organization
Computer = CPU + Memory + I/O
bus – a series of parallel wires used to transmit data

## Slide 10: Instructions and Datapath
There are two types of instructions that the CPU can execute:
Register-Memory
  can load words into registers
  store words back into memory
Register-Register
The datapath consists of the ALU and registers. This datapath usually goes through the following cycle (called, appropriately, a datapath cycle) for a register-register instruction:
Run two operands on ALU
Store the result back into the registers
This process determines the speed of the processor.

## Slide 11: Instruction Execution
All instructions are executed like so:
Fetch next instruction to Instruction Register
Change Program Counter to point to the next instruction
Determine instruction type (decode)
[If needed] Calculate memory address
[If needed] Fetch word into CPU register
Execute Instruction
Repeat
Note: the instructions and addresses must already be in the registers of the CPU in order for the ALU to do calculations, particularly in steps 2, 3, and 4.

## Slide 12: RISC vs. CISC
Reduced Instruction Set Computer
make the common case fast; small and simple instruction set
more instructions needed to do something
all instructions can execute in one clock cycle
Complex Instruction Set Computer
large and varied instruction set
fewer instructions needed to do something
takes longer because of interpretation; multiple clock cycles

## Slide 13: Design Principles for Modern Computers
For general-purpose modern CPUs that follow RISC, these are the design principles which are desired:
All instructions are directly executed by hardware.
  eliminating a level of interpretation allows for higher speeds
Maximize the rate at which instructions are issued.
  execute instructions in parallel to make the computer faster and efficient
Instructions should be easy to decode.
  instructions represent control signals for datapath units; the simpler, the better
Only LOAD and STORE instructions should reference memory.
  referencing memory takes a long time, so only few instructions should
  everything else is through registers
Provide plenty of registers.
  if all registers are used, flushing out to memory and then reloading is expensive!

## Slide 14: Parallelism
There are two types of parallelism for faster computers:
Instruction-Level Parallelism
Processor-Level Parallelism

## Slide 15: Instruction-Level Parallelism
Instruction-Level Parallelism aims to do more instructions per second. This is mostly achieved through pipelining and superscalar architecture.
pipelining – overlapping different processes
  improving latency (how long it takes to execute an instruction) and throughput (how often an instruction is completed)
superscalar architecture – issue multiple instructions in one clock cycle

## Slide 16: Processor-Level Parallelism
Processor-Level Parallelism aims to use more CPUs for the same problem. There are a couple of ways to achieve this:
SIMD Processor – many identical processors perform the same sequence of instructions on different sets of data
Vector Processor – all operations are performed in a single, pipelined unit
Multiprocessor – a system with more than one CPU sharing a memory
Multicomputers – a system with multiple CPUS, each with own local memory

## Slide 17: Memory and Memory Addresses
A memory consists of a number of cells m, each with an address from 0 to m – 1. Each cell has n bits.
An m × n memory
needs log2m addresses
..................
m cells
n-bits per cell
Address
0
1
m – 2
m – 1
Standard is usually an 8-bit cell, or a byte.

## Slide 18: Byte Ordering
Big Endian | stores most significant byte in | smallest | address
Little Endian |  | largest | 
address | memory
a | 0A
a + 1 | 0B
a + 2 | 0C
... | ...
Outside of registers, this is how bytes are stored in hardware/memory.
memory | address
0C | a
0B | a + 1
0A | a + 2
... | ...
Big Endian
Little Endian
Register
0A | 0B | 0C

## Slide 19: Memory Hierarchy
CPUs are faster than memory, so if the memory is really slow, the CPU has to wait for a lot of cycles. Thus, we want a lot of memory to store information, and we want it to be fast. However, fast memory is expensive!
How do we make it so that memory is big, fast, and cheap? A memory hierarchy:
Registers
Cache
RAM and Virtual Memory
Hard Disks
Input Sources
Primary Memory
fast, small, expensive,
close to CPU
volatile
Secondary Memory
slow, large, cheap,
far from CPU,
permanent/non-volatile besides RAM
As you go down,
three factors increase:
access time
storage capacity
bits per dollar

## Slide 20: Caches
This is the solution: combine a small amount of fast memory with a large amount of slow memory. In the cache, the most heavily used memory words are kept; when the CPU needs a word, it will look here BEFORE it looks at main memory.
locality principle – when a word is referenced, it and some of its neighbors are brought into the cache
cache lines – fixed-size blocks in the cache; a miss means a whole cache line is taken in from main memory
Unified Cache | stores instructions and data in | same | cache
Split Cache |  | separate | 

## Slide 21: III. The Digital Logic Level

## Slide 22: Boolean Algebra
I’m not wasting my time on this. You guys should’ve taken ICS 6B.
Know the AND and OR gates, truth tables, and sum of products form.

## Slide 23: Combinational Circuits
A combinational circuit is a circuit with multiple inputs and outputs in which the outputs are uniquely determined by the current input values
these circuits flow only in one direction
as such, no value is remembered
e.g. Selectors/Multiplexers, Encoders/Decoders, Full-Adders

## Slide 24: Selectors/Multiplexers
Given multiple inputs, how do we get only one through to output?
We use select lines!
2n-to-1 Multiplexer
...
2n data inputs
n control bits or
select lines
1 output

## Slide 25: Encoders
Given 2n inputs, creates an n-bit binary number as output along with a valid output which says whether there is at least one input of 1 (otherwise, all are 0).
...
2n data inputs
n-bit binary number
2n-to-n Encoder
...
V
Note: inputs with higher position
have encoding priority

## Slide 26: Decoders
Given an n-bit binary number, decodes into 2n outputs, with only one output being asserted at any time (i.e. only one output is 1).
...
2n outputs
n-bit binary number
n-to-2n Decoder
...

## Slide 27: Full-Adders
Takes in three inputs: two 1-bit integers to add and a carry-in. This, in turn, produces two outputs: one 1-bit sum and a carry-out.
1-bit
Full-Adder
A
B
carry-in
sum
carry-out
Note: can combine n 1-bit Full-Adders to
create an n-bit Full-Adder
1-bit FA
carry-in
A0
B0
1-bit FA
carry
A1
B1
1-bit FA
carry
A2
B2
carry-out
S2
S1
S0
3-bit
Full-Adder
A2:A0
carry-in
carry-out
B2:B0
S2:S0

## Slide 28: Clocks
A clock is a circuit that emits a series of pulses with a precise pulse width and precise interval – which is the clock cycle time – between consecutive pulses. This interval is constant, which makes clocks symmetric (i.e. time spent on = time spent off).
Pulse Frequencies are measured in Megahertz (MHz) or Gigahertz (GHz), which correspond to clock cycle times (usually in nanoseconds). These units refer to the speeds of the processor
Clock = 1 (ON)
Clock = 0 (OFF)
rising edge
falling edge

## Slide 29: Sequential Circuits and Memory
A sequential circuit combines a combinational circuit with a clock, which allows the circuit to “remember” what the previous value was. This is achieved so that we can make memory, which is used to store data in computers.
To make memory, we need to do the following:
Build a 1-bit memory component
Combine memory components for a register
Combine registers for a register file

## Slide 30: 1. Build a 1-bit memory component
This requires the following steps:
Create an SR Latch
Create a D-Latch
Create a Clocked D-Latch
Create a D-Flip-Flop
Note that, with regards to clocks, latches are level-triggered whereas flip-flops are edge-triggered.

## Slide 31: A. Create an SR Latch
1-bit storage component that stores a value using a feedback loop
inputs:
  S (set) – returns if Q is 1
  R (reset) – returns if Q is 0
outputs are Q and Q’
 | S | R | Qprev | Q | Q’
hold old value of Q is saved | 0 | 0 | 0 | 0 | 1
 | 0 | 0 | 1 | 1 | 0
reset Q = 0 | 0 | 1 | 0 | 0 | 1
 | 0 | 1 | 1 | 0 | 1
set Q = 1 | 1 | 0 | 0 | 1 | 0
 | 1 | 0 | 1 | 1 | 0
invalid cannot happen! | 1 | 1 | 0 | 0 | 0
 | 1 | 1 | 1 | 0 | 0

## Slide 32: B. Create a D-Latch
1-bit asynchronous storage component
  asynchronous – output changes as soon as input changes
input is 1-bit data input D
outputs are Q and Q’ (Q is the value of D)
  Note: guaranteed valid input with the NOT gate
SR Latch
D
Q
Q’
S
R

## Slide 33: C. Create a Clocked D-Latch
1-bit synchronous storage component
  synchronous – output changes based on a clock signal
level-triggered – Q is updated during the level of the clock
SR Latch
D
Q
Q’
S
R
Q = D
Q = Q
Q = Q
Q = Q
Q = D
Q = D
Q = D

## Slide 34: D. Create a Clocked D-Flip-Flop
1-bit asynchronous storage component
  storage happens in an instant!
edge-triggered – Q is updated during the clock transitions (i.e. edges)
  for this flip-flop, it will only happen at the rising edge since there is a delay on the gates!
Clocked D-Latch
D
Q
Q’
D
Clock
Q = D
Q = D
Q = D
Q = D

## Slide 35: 2. Combine memory components for a register
A register is an n-bit storage component which can be made out of D-Flip-Flops, like so:
D-Flip-Flop
Q
D
Clock
D0
Q0
D-Flip-Flop
Q
D
Clock
D1
Q1
D-Flip-Flop
Q
D
Clock
Dn – 1
Qn – 1
...
Note: All the clocks are synchronized to one clock signal in a register!
An n-bit register
clock signal

## Slide 36: 3. Combine registers for a register file
A register file holds a number of registers inside it, each which take in the same number of bits (called the register width).
An m × n register file, where m is the number of registers and n is the width, is organized as such:
Q
D
Clk
An m × n register file
Q
D
Clk
Q
D
Clk
...
Q
D
Clk
Q
D
Clk
Q
D
Clk
...
..................
m registers
Register 0
Register m – 1
n-bits per register

## Slide 37: Memory Organization
How do you choose what registers to read/write in for a register file, especially if for reading, we want just one output? We use signals!
An m × n register file
Alog m – 1:A0
Chip Select
Read/!Write
Output Enable
On – 1:O0
In – 1:I0
Address of Registers, given as a log2m-bit number; this will be decoded to m outputs which signify which register is used.
Chip Select signals whether a register
is to be used (either reading or writing); 1 means yes, 0 means no.
Read/!Write signals whether a register, if selected, is to be read (1) or written (0).
Output Enable signals whether output will be given; will give output if chip select and read are also 1.
Note: enabling output requires a
non-inverting buffer, like so:
input
output
enable; will send output only if 1

## Slide 38: IV. Microarchitecture

## Slide 39: Microarchitecture Design and IJVM
Every Instruction Set Architecture (ISA) requires a different microarchitecture – meaning there aren’t any general principles.
As such, we can study a specific microarchitecture called the Integer Java Virtual Machine (IJVM), which contains a microprogram that does the following for IJVM instructions:
fetch
decode
execute
The microprogram also has a set of variables (state), accessible by all functions.

## Slide 40: IJVM Instructions
Opcode • identifies the instruction | Operand • identifies register location, variable, etc.
IJVM instructions usually have these two fields:
These are executed by the microprogram through a series of microinstructions. In general,
a = 10
High-Level Instruction
BIPUSH 10
ISTORE a
IJVM ISA Instructions
bipush1
bipush2
...
Microinstructions
compiler
microprogram

## Slide 41: IJVM Datapath
The datapath of an IJVM processor consists of the following:
32-bit registers
B-Bus – contents of the registers
C-Bus – output of the ALU; can write to multiple registers
ALU – contains two inputs:
  A (register H; 1 source)
  B (bus B; 9 possible sources)

## Slide 42: IJVM Datapath Timing
Starting from the falling edge of the clock and ending at the rising edge of the clock, the bus clock cycle follows the diagram below:
This allows for a register to be read
AND written in the same cycle; 1st half
of cycle you read (with B bus), and 2nd half
you write (with C bus).
The implementation requires
rigid timing
long clock cycles
known minimum propagation delay
fast load of registers from C-Bus

## Slide 43: IJVM Memory Registers
MAR – contains the word address for MDR
MDR – contains the word itself
PC – contains the byte address for MBR
MBR – contains the byte itself
Note: the MBR has additional signals to tell the bus if its value is positive or negative!
32-bit registers to read/write
ISA-level data words
8-bit registers to read only
the executable ISA program

## Slide 44: IJVM Microinstruction Signals
Controlling the datapath in one cycle needs 29 signals, split into five:
9 Signals to write C bus –> registers | 9 Signals to enable registers –> B bus for ALU | 8 Signals to control ALU and shifter | 2 Signals to indicate memory read/write | 1 Signal to indicate memory fetch
We can write into multiple registers with C-Bus, but we CANNOT read into multiple registers with B-Bus. As such, we can decrease the number of signals for the B-Bus to 4 and use a decoder instead.

## Slide 45: IJVM Microinstruction Signals (Continued)
Adding 9 more signals for the address of the next microinstruction and 3 more signals for how to select the next microinstruction, we have 36 total signals to format into a microinstruction:
JAM:
N = is ALU result negative
Z = is ALU result 0
Memory:
Each function takes 3 bus cycles.
get address
read, write, fetch on memory
now usable

## Slide 46: IJVM Sequencer and Control Store
These microinstructions are fetched by the sequencer from the control store ( a read-only memory), which holds a microprogram along with the Microinstruction Register (MIR) and the Microprogram Counter (MPC). Every cycle, this happens:
MIR is loaded from the word pointed by MPC in the control store (∆w)
NEXT_ADDRESS is copied to MPC while JAM is examined
  If JAMZ or JAMN is set (1), then the respective flip-flop (which saves whether the ALU output is 0/negative) is ORed into the high-order bit of MPC
  MPC now has NEXT_ADDRESS with the high-order bit either 0 (no jams) or 1 (jams)
  This allows for jumps/conditionals
Now, MPC has the next instruction to do.
Note that the sequencer produces two types of information: the state of every signal in the system and the address of the next instruction.

## Slide 47: IJVM Stack-Based Machine
There are two more registers that are used to hold the local variables of a procedure/IJVM instruction:
SP – pointer to top of the stack
  changes anytime something is pushed/popped
LV – pointer to local variables
  changes when another procedure is called; otherwise, does not change!
The stack is also used to hold operands during computation of arithmetic expressions, which are usually done through IJVM instructions.

## Slide 48: Example MIC-1 Simulation
For the high level code
c = a + b
Do the following:
Create the corresponding IJVM hex code.
Store it into appropriate cells.
Simulate each instruction.
Show changing contents of the data cell.
 |  |  | 0x18 |  |  PC
0xC80 |  |  SP | 0x19 |  | 
0xC84 |  |  | 0x1A |  | 
0xC88 |  |  | 0x1B |  | 
 |  |  | 0x1C |  | 
 |  |  | 0x1D |  | 
 |  |  | 0x1E |  | 
 |  |  | 0x1F |  | 
 |  |  | 0x20 |  | 
0xE10 | a: 6 |  LV | 0x21 |  | 
0xE14 | b: 10 |  | 0x22 |  | 
0xE18 | c: 8 |  | 0x23 |  | 
 |  |  | 0x24 |  | 
 |  |  | 0x25 |  | 
 |  |  | 0x26 |  | 

## Slide 49: 1. Create the corresponding IJVM hex code.
c = a + b
Hex | Mnemonic | Meaning
0x60 | IADD | Pop two words from stack; push their sum
0x15 | ILOAD varnum | Push local variable onto stack
0x36 | ISTORE varnum | Pop word from stack and store in local variable
From the IJVM MIC-1 Instructions, we can deconstruct the high-level code to the following:
IJVM Instruction | Hex Codes
ILOAD a | 0x15 0x00
ILOAD b | 0x15 0x01
IADD | 0x60
ISTORE c | 0x36 0x02
The italicized hex codes represent the offset from LV.

## Slide 50: 2. Store it into appropriate cells.
With the hex codes from the previous step, we can now fill out the method area (which the PC points to) with the program, like so:
0x18 | 0x15 |  PC
0x19 | 0x00 | 
0x1A | 0x15 | 
0x1B | 0x01 | 
0x1C | 0x60 | 
0x1D | 0x36 | 
0x1E | 0x02 | 
0x1F |  | 
0x20 |  | 
0x21 |  | 
0x22 |  | 
0x23 |  | 
0x24 |  | 
0x25 |  | 
0x26 |  | 
IJVM Instruction | Hex Codes
ILOAD a | 0x15 0x00
ILOAD b | 0x15 0x01
IADD | 0x60
ISTORE c | 0x36 0x02

## Slide 51: 3. Simulate each instruction.
We can now simulate each instruction with the information we have.
With the given IJVM instructions, we can examine the microprogram for MIC-1 and see what microinstructions we have to carry out.
Label | Operations
Main1 | PC = PC + 1; fetch; goto (MBR)
iadd1 | MAR = SP = SP – 1; rd
iadd2 | H = TOS
iadd3 | MDR = TOS = MDR + H; wr; goto Main1
iload1 | H = LV
iload2 | MAR = MBRU + H; rd
iload3 | MAR = SP = SP + 1
iload4 | PC = PC + 1; fetch; wr
iload5 | TOS = MDR; goto Main1
istore1 | H = LV
istore2 | MAR = MBRU + H
istore3 | MDR = TOS; wr
istore4 | SP = MAR = SP – 1; rd
istore5 | PC = PC + 1; fetch
istore6 | TOS = MDR; goto Main1
Note:
read – MDR = MEM[MAR]32
write – MEM[MAR]32 = MDR
fetch – MBR = MEM[PC]8

## Slide 52
Here is the order of the microinstructions based on our method area:
0x18 | 0x15 |  PC
0x19 | 0x00 | 
0x1A | 0x15 | 
0x1B | 0x01 | 
0x1C | 0x60 | 
0x1D | 0x36 | 
0x1E | 0x02 | 
0x1F |  | 
0x20 |  | 
0x21 |  | 
0x22 |  | 
0x23 |  | 
0x24 |  | 
0x25 |  | 
0x26 |  | 
Main1
iload1
iload2
iload3
iload4
iload5
Main1
iload1
iload2
iload3
iload4
iload5
Main1
iadd1
iadd2
iadd3
Main1
istore1
istore2
istore3
istore4
istore5
istore6

## Slide 53
All of the registers and cells before the simulation begins:
 |  |  | 0x18 | 0x15 |  PC
0xC80 |  |  SP | 0x19 | 0x00 | 
0xC84 |  |  | 0x1A | 0x15 | 
0xC88 |  |  | 0x1B | 0x01 | 
 |  |  | 0x1C | 0x60 | 
 |  |  | 0x1D | 0x36 | 
 |  |  | 0x1E | 0x02 | 
 |  |  | 0x1F |  | 
 |  |  | 0x20 |  | 
0xE10 | a: 6 |  LV | 0x21 |  | 
0xE14 | b: 10 |  | 0x22 |  | 
0xE18 | c: 8 |  | 0x23 |  | 
 |  |  | 0x24 |  | 
 |  |  | 0x25 |  | 
 |  |  | 0x26 |  | 
REGISTER FILE CONTENTS | 
MAR | ?
MDR | ?
PC | 0x18
MBR | 0x15
SP | 0xC80
TOS | ?
LV | 0xE10
H | ?

## Slide 54
1. Main1: PC = PC + 1; fetch; goto (MBR)
 |  |  | 0x18 | 0x15 | 
0xC80 |  |  SP | 0x19 | 0x00 |  PC
0xC84 |  |  | 0x1A | 0x15 | 
0xC88 |  |  | 0x1B | 0x01 | 
 |  |  | 0x1C | 0x60 | 
 |  |  | 0x1D | 0x36 | 
 |  |  | 0x1E | 0x02 | 
 |  |  | 0x1F |  | 
 |  |  | 0x20 |  | 
0xE10 | a: 6 |  LV | 0x21 |  | 
0xE14 | b: 10 |  | 0x22 |  | 
0xE18 | c: 8 |  | 0x23 |  | 
 |  |  | 0x24 |  | 
 |  |  | 0x25 |  | 
 |  |  | 0x26 |  | 
REGISTER FILE CONTENTS | 
MAR | ?
MDR | ?
PC | 0x18/0x19
MBR | 0x15
SP | 0xC80
TOS | ?
LV | 0xE10
H | ?

## Slide 55
2. iload1: H = LV
 |  |  | 0x18 | 0x15 | 
0xC80 |  |  SP | 0x19 | 0x00 |  PC
0xC84 |  |  | 0x1A | 0x15 | 
0xC88 |  |  | 0x1B | 0x01 | 
 |  |  | 0x1C | 0x60 | 
 |  |  | 0x1D | 0x36 | 
 |  |  | 0x1E | 0x02 | 
 |  |  | 0x1F |  | 
 |  |  | 0x20 |  | 
0xE10 | a: 6 |  LV | 0x21 |  | 
0xE14 | b: 10 |  | 0x22 |  | 
0xE18 | c: 8 |  | 0x23 |  | 
 |  |  | 0x24 |  | 
 |  |  | 0x25 |  | 
 |  |  | 0x26 |  | 
REGISTER FILE CONTENTS | 
MAR | ?
MDR | ?
PC | 0x18/0x19
MBR | 0x15/0x00
SP | 0xC80
TOS | ?
LV | 0xE10
H | ?/0xE10

## Slide 56
3. iload2: MAR = MBRU + H; rd
 |  |  | 0x18 | 0x15 | 
0xC80 |  |  SP | 0x19 | 0x00 |  PC
0xC84 |  |  | 0x1A | 0x15 | 
0xC88 |  |  | 0x1B | 0x01 | 
 |  |  | 0x1C | 0x60 | 
 |  |  | 0x1D | 0x36 | 
 |  |  | 0x1E | 0x02 | 
 |  |  | 0x1F |  | 
 |  |  | 0x20 |  | 
0xE10 | a: 6 |  LV | 0x21 |  | 
0xE14 | b: 10 |  | 0x22 |  | 
0xE18 | c: 8 |  | 0x23 |  | 
 |  |  | 0x24 |  | 
 |  |  | 0x25 |  | 
 |  |  | 0x26 |  | 
REGISTER FILE CONTENTS | 
MAR | ?/0xE10
MDR | ?
PC | 0x18/0x19
MBR | 0x15/0x00
SP | 0xC80
TOS | ?
LV | 0xE10
H | ?/0xE10

## Slide 57
4. iload3: MAR = SP = SP + 1
 |  |  | 0x18 | 0x15 | 
0xC80 |  |  | 0x19 | 0x00 |  PC
0xC84 |  |  SP | 0x1A | 0x15 | 
0xC88 |  |  | 0x1B | 0x01 | 
 |  |  | 0x1C | 0x60 | 
 |  |  | 0x1D | 0x36 | 
 |  |  | 0x1E | 0x02 | 
 |  |  | 0x1F |  | 
 |  |  | 0x20 |  | 
0xE10 | a: 6 |  LV | 0x21 |  | 
0xE14 | b: 10 |  | 0x22 |  | 
0xE18 | c: 8 |  | 0x23 |  | 
 |  |  | 0x24 |  | 
 |  |  | 0x25 |  | 
 |  |  | 0x26 |  | 
REGISTER FILE CONTENTS | 
MAR | ?/0xE10/0xC84
MDR | ?/6
PC | 0x18/0x19
MBR | 0x15/0x00
SP | 0xC80/0xC84
TOS | ?
LV | 0xE10
H | ?/0xE10

## Slide 58
5. iload4: PC = PC + 1; fetch; wr
 |  |  | 0x18 | 0x15 | 
0xC80 |  |  | 0x19 | 0x00 | 
0xC84 |  |  SP | 0x1A | 0x15 |  PC
0xC88 |  |  | 0x1B | 0x01 | 
 |  |  | 0x1C | 0x60 | 
 |  |  | 0x1D | 0x36 | 
 |  |  | 0x1E | 0x02 | 
 |  |  | 0x1F |  | 
 |  |  | 0x20 |  | 
0xE10 | a: 6 |  LV | 0x21 |  | 
0xE14 | b: 10 |  | 0x22 |  | 
0xE18 | c: 8 |  | 0x23 |  | 
 |  |  | 0x24 |  | 
 |  |  | 0x25 |  | 
 |  |  | 0x26 |  | 
REGISTER FILE CONTENTS | 
MAR | ?/0xE10/0xC84
MDR | ?/6
PC | 0x18/0x19/0x1A
MBR | 0x15/0x00
SP | 0xC80/0xC84
TOS | ?
LV | 0xE10
H | ?/0xE10

## Slide 59
6. iload5: TOS = MDR; goto Main1
 |  |  | 0x18 | 0x15 | 
0xC80 |  |  | 0x19 | 0x00 | 
0xC84 | 6 |  SP | 0x1A | 0x15 |  PC
0xC88 |  |  | 0x1B | 0x01 | 
 |  |  | 0x1C | 0x60 | 
 |  |  | 0x1D | 0x36 | 
 |  |  | 0x1E | 0x02 | 
 |  |  | 0x1F |  | 
 |  |  | 0x20 |  | 
0xE10 | a: 6 |  LV | 0x21 |  | 
0xE14 | b: 10 |  | 0x22 |  | 
0xE18 | c: 8 |  | 0x23 |  | 
 |  |  | 0x24 |  | 
 |  |  | 0x25 |  | 
 |  |  | 0x26 |  | 
REGISTER FILE CONTENTS | 
MAR | ?/0xE10/0xC84
MDR | ?/6
PC | 0x18/0x19/0x1A
MBR | 0x15/0x00/0x15
SP | 0xC80/0xC84
TOS | ?/6
LV | 0xE10
H | ?/0xE10

## Slide 60
7. Main1: PC = PC + 1; fetch; goto (MBR)
 |  |  | 0x18 | 0x15 | 
0xC80 |  |  | 0x19 | 0x00 | 
0xC84 | 6 |  SP | 0x1A | 0x15 | 
0xC88 |  |  | 0x1B | 0x01 |  PC
 |  |  | 0x1C | 0x60 | 
 |  |  | 0x1D | 0x36 | 
 |  |  | 0x1E | 0x02 | 
 |  |  | 0x1F |  | 
 |  |  | 0x20 |  | 
0xE10 | a: 6 |  LV | 0x21 |  | 
0xE14 | b: 10 |  | 0x22 |  | 
0xE18 | c: 8 |  | 0x23 |  | 
 |  |  | 0x24 |  | 
 |  |  | 0x25 |  | 
 |  |  | 0x26 |  | 
REGISTER FILE CONTENTS | 
MAR | ?/0xE10/0xC84
MDR | ?/6
PC | 0x18/0x19/0x1A/0x1B
MBR | 0x15/0x00/0x15
SP | 0xC80/0xC84
TOS | ?/6
LV | 0xE10
H | ?/0xE10

## Slide 61
8. iload1: H = LV
 |  |  | 0x18 | 0x15 | 
0xC80 |  |  | 0x19 | 0x00 | 
0xC84 | 6 |  SP | 0x1A | 0x15 | 
0xC88 |  |  | 0x1B | 0x01 |  PC
 |  |  | 0x1C | 0x60 | 
 |  |  | 0x1D | 0x36 | 
 |  |  | 0x1E | 0x02 | 
 |  |  | 0x1F |  | 
 |  |  | 0x20 |  | 
0xE10 | a: 6 |  LV | 0x21 |  | 
0xE14 | b: 10 |  | 0x22 |  | 
0xE18 | c: 8 |  | 0x23 |  | 
 |  |  | 0x24 |  | 
 |  |  | 0x25 |  | 
 |  |  | 0x26 |  | 
REGISTER FILE CONTENTS | 
MAR | ?/0xE10/0xC84
MDR | ?/6
PC | 0x18/0x19/0x1A/0x1B
MBR | 0x15/0x00/0x15/0x01
SP | 0xC80/0xC84
TOS | ?/6
LV | 0xE10
H | ?/0xE10/0xE10

## Slide 62
9. iload2: MAR = MBRU + H; rd
 |  |  | 0x18 | 0x15 | 
0xC80 |  |  | 0x19 | 0x00 | 
0xC84 | 6 |  SP | 0x1A | 0x15 | 
0xC88 |  |  | 0x1B | 0x01 |  PC
 |  |  | 0x1C | 0x60 | 
 |  |  | 0x1D | 0x36 | 
 |  |  | 0x1E | 0x02 | 
 |  |  | 0x1F |  | 
 |  |  | 0x20 |  | 
0xE10 | a: 6 |  LV | 0x21 |  | 
0xE14 | b: 10 |  | 0x22 |  | 
0xE18 | c: 8 |  | 0x23 |  | 
 |  |  | 0x24 |  | 
 |  |  | 0x25 |  | 
 |  |  | 0x26 |  | 
REGISTER FILE CONTENTS | 
MAR | ?/0xE10/0xC84/0xE14
MDR | ?/6
PC | 0x18/0x19/0x1A/0x1B
MBR | 0x15/0x00/0x15/0x01
SP | 0xC80/0xC84
TOS | ?/6
LV | 0xE10
H | ?/0xE10/0xE10

## Slide 63
10. iload3: MAR = SP = SP + 1
 |  |  | 0x18 | 0x15 | 
0xC80 |  |  | 0x19 | 0x00 | 
0xC84 | 6 |  | 0x1A | 0x15 | 
0xC88 |  |  SP | 0x1B | 0x01 |  PC
 |  |  | 0x1C | 0x60 | 
 |  |  | 0x1D | 0x36 | 
 |  |  | 0x1E | 0x02 | 
 |  |  | 0x1F |  | 
 |  |  | 0x20 |  | 
0xE10 | a: 6 |  LV | 0x21 |  | 
0xE14 | b: 10 |  | 0x22 |  | 
0xE18 | c: 8 |  | 0x23 |  | 
 |  |  | 0x24 |  | 
 |  |  | 0x25 |  | 
 |  |  | 0x26 |  | 
REGISTER FILE CONTENTS | 
MAR | ?/0xE10/0xC84/0xE14/0xC88
MDR | ?/6/10
PC | 0x18/0x19/0x1A/0x1B
MBR | 0x15/0x00/0x15/0x01
SP | 0xC80/0xC84/0xC88
TOS | ?/6
LV | 0xE10
H | ?/0xE10/0xE10

## Slide 64
11. iload4: PC = PC + 1; fetch; wr
 |  |  | 0x18 | 0x15 | 
0xC80 |  |  | 0x19 | 0x00 | 
0xC84 | 6 |  | 0x1A | 0x15 | 
0xC88 |  |  SP | 0x1B | 0x01 | 
 |  |  | 0x1C | 0x60 |  PC
 |  |  | 0x1D | 0x36 | 
 |  |  | 0x1E | 0x02 | 
 |  |  | 0x1F |  | 
 |  |  | 0x20 |  | 
0xE10 | a: 6 |  LV | 0x21 |  | 
0xE14 | b: 10 |  | 0x22 |  | 
0xE18 | c: 8 |  | 0x23 |  | 
 |  |  | 0x24 |  | 
 |  |  | 0x25 |  | 
 |  |  | 0x26 |  | 
REGISTER FILE CONTENTS | 
MAR | ?/0xE10/0xC84/0xE14/0xC88
MDR | ?/6/10
PC | 0x18/0x19/0x1A/0x1B/0x1C
MBR | 0x15/0x00/0x15/0x01
SP | 0xC80/0xC84/0xC88
TOS | ?/6
LV | 0xE10
H | ?/0xE10/0xE10

## Slide 65
12. iload5: TOS = MDR; goto Main1
 |  |  | 0x18 | 0x15 | 
0xC80 |  |  | 0x19 | 0x00 | 
0xC84 | 6 |  | 0x1A | 0x15 | 
0xC88 | 10 |  SP | 0x1B | 0x01 | 
 |  |  | 0x1C | 0x60 |  PC
 |  |  | 0x1D | 0x36 | 
 |  |  | 0x1E | 0x02 | 
 |  |  | 0x1F |  | 
 |  |  | 0x20 |  | 
0xE10 | a: 6 |  LV | 0x21 |  | 
0xE14 | b: 10 |  | 0x22 |  | 
0xE18 | c: 8 |  | 0x23 |  | 
 |  |  | 0x24 |  | 
 |  |  | 0x25 |  | 
 |  |  | 0x26 |  | 
REGISTER FILE CONTENTS | 
MAR | ?/0xE10/0xC84/0xE14/0xC88
MDR | ?/6/10
PC | 0x18/0x19/0x1A/0x1B/0x1C
MBR | 0x15/0x00/0x15/0x01/0x60
SP | 0xC80/0xC84/0xC88
TOS | ?/6/10
LV | 0xE10
H | ?/0xE10/0xE10

## Slide 66
13. Main1: PC = PC + 1; fetch; goto (MBR)
 |  |  | 0x18 | 0x15 | 
0xC80 |  |  | 0x19 | 0x00 | 
0xC84 | 6 |  | 0x1A | 0x15 | 
0xC88 | 10 |  SP | 0x1B | 0x01 | 
 |  |  | 0x1C | 0x60 | 
 |  |  | 0x1D | 0x36 |  PC
 |  |  | 0x1E | 0x02 | 
 |  |  | 0x1F |  | 
 |  |  | 0x20 |  | 
0xE10 | a: 6 |  LV | 0x21 |  | 
0xE14 | b: 10 |  | 0x22 |  | 
0xE18 | c: 8 |  | 0x23 |  | 
 |  |  | 0x24 |  | 
 |  |  | 0x25 |  | 
 |  |  | 0x26 |  | 
REGISTER FILE CONTENTS | 
MAR | ?/0xE10/0xC84/0xE14/0xC88
MDR | ?/6/10
PC | 0x18/0x19/0x1A/0x1B/0x1C/0x1D
MBR | 0x15/0x00/0x15/0x01/0x60
SP | 0xC80/0xC84/0xC88
TOS | ?/6/10
LV | 0xE10
H | ?/0xE10/0xE10

## Slide 67
14. iadd1: MAR = SP = SP – 1; rd
 |  |  | 0x18 | 0x15 | 
0xC80 |  |  | 0x19 | 0x00 | 
0xC84 | 6 |  SP | 0x1A | 0x15 | 
0xC88 | 10 |  | 0x1B | 0x01 | 
 |  |  | 0x1C | 0x60 | 
 |  |  | 0x1D | 0x36 |  PC
 |  |  | 0x1E | 0x02 | 
 |  |  | 0x1F |  | 
 |  |  | 0x20 |  | 
0xE10 | a: 6 |  LV | 0x21 |  | 
0xE14 | b: 10 |  | 0x22 |  | 
0xE18 | c: 8 |  | 0x23 |  | 
 |  |  | 0x24 |  | 
 |  |  | 0x25 |  | 
 |  |  | 0x26 |  | 
REGISTER FILE CONTENTS | 
MAR | ?/0xE10/0xC84/0xE14/0xC88/0xC84
MDR | ?/6/10
PC | 0x18/0x19/0x1A/0x1B/0x1C/0x1D
MBR | 0x15/0x00/0x15/0x01/0x60/0x36
SP | 0xC80/0xC84/0xC88/0xC84
TOS | ?/6/10
LV | 0xE10
H | ?/0xE10/0xE10

## Slide 68
15. iadd2: H = TOS
 |  |  | 0x18 | 0x15 | 
0xC80 |  |  | 0x19 | 0x00 | 
0xC84 | 6 |  SP | 0x1A | 0x15 | 
0xC88 | 10 |  | 0x1B | 0x01 | 
 |  |  | 0x1C | 0x60 | 
 |  |  | 0x1D | 0x36 |  PC
 |  |  | 0x1E | 0x02 | 
 |  |  | 0x1F |  | 
 |  |  | 0x20 |  | 
0xE10 | a: 6 |  LV | 0x21 |  | 
0xE14 | b: 10 |  | 0x22 |  | 
0xE18 | c: 8 |  | 0x23 |  | 
 |  |  | 0x24 |  | 
 |  |  | 0x25 |  | 
 |  |  | 0x26 |  | 
REGISTER FILE CONTENTS | 
MAR | ?/0xE10/0xC84/0xE14/0xC88/0xC84
MDR | ?/6/10/6
PC | 0x18/0x19/0x1A/0x1B/0x1C/0x1D
MBR | 0x15/0x00/0x15/0x01/0x60/0x36
SP | 0xC80/0xC84/0xC88/0xC84
TOS | ?/6/10
LV | 0xE10
H | ?/0xE10/0xE10/10

## Slide 69
16. iadd3: MDR = TOS = MDR + H; wr; goto Main1
 |  |  | 0x18 | 0x15 | 
0xC80 |  |  | 0x19 | 0x00 | 
0xC84 | 6 |  SP | 0x1A | 0x15 | 
0xC88 | 10 |  | 0x1B | 0x01 | 
 |  |  | 0x1C | 0x60 | 
 |  |  | 0x1D | 0x36 |  PC
 |  |  | 0x1E | 0x02 | 
 |  |  | 0x1F |  | 
 |  |  | 0x20 |  | 
0xE10 | a: 6 |  LV | 0x21 |  | 
0xE14 | b: 10 |  | 0x22 |  | 
0xE18 | c: 8 |  | 0x23 |  | 
 |  |  | 0x24 |  | 
 |  |  | 0x25 |  | 
 |  |  | 0x26 |  | 
REGISTER FILE CONTENTS | 
MAR | ?/0xE10/0xC84/0xE14/0xC88/0xC84
MDR | ?/6/10/6/16
PC | 0x18/0x19/0x1A/0x1B/0x1C/0x1D
MBR | 0x15/0x00/0x15/0x01/0x60/0x36
SP | 0xC80/0xC84/0xC88/0xC84
TOS | ?/6/10/16
LV | 0xE10
H | ?/0xE10/0xE10/10

## Slide 70
17. Main1: PC = PC + 1; fetch; goto (MBR)
 |  |  | 0x18 | 0x15 | 
0xC80 |  |  | 0x19 | 0x00 | 
0xC84 | 16 |  SP | 0x1A | 0x15 | 
0xC88 | 10 |  | 0x1B | 0x01 | 
 |  |  | 0x1C | 0x60 | 
 |  |  | 0x1D | 0x36 | 
 |  |  | 0x1E | 0x02 |  PC
 |  |  | 0x1F |  | 
 |  |  | 0x20 |  | 
0xE10 | a: 6 |  LV | 0x21 |  | 
0xE14 | b: 10 |  | 0x22 |  | 
0xE18 | c: 8 |  | 0x23 |  | 
 |  |  | 0x24 |  | 
 |  |  | 0x25 |  | 
 |  |  | 0x26 |  | 
REGISTER FILE CONTENTS | 
MAR | ?/0xE10/0xC84/0xE14/0xC88/0xC84
MDR | ?/6/10/6/16
PC | 0x18/0x19/0x1A/0x1B/0x1C/0x1D/0x1E
MBR | 0x15/0x00/0x15/0x01/0x60/0x36
SP | 0xC80/0xC84/0xC88/0xC84
TOS | ?/6/10/16
LV | 0xE10
H | ?/0xE10/0xE10/10

## Slide 71
18. istore1: H = LV
 |  |  | 0x18 | 0x15 | 
0xC80 |  |  | 0x19 | 0x00 | 
0xC84 | 16 |  SP | 0x1A | 0x15 | 
0xC88 | 10 |  | 0x1B | 0x01 | 
 |  |  | 0x1C | 0x60 | 
 |  |  | 0x1D | 0x36 | 
 |  |  | 0x1E | 0x02 |  PC
 |  |  | 0x1F |  | 
 |  |  | 0x20 |  | 
0xE10 | a: 6 |  LV | 0x21 |  | 
0xE14 | b: 10 |  | 0x22 |  | 
0xE18 | c: 8 |  | 0x23 |  | 
 |  |  | 0x24 |  | 
 |  |  | 0x25 |  | 
 |  |  | 0x26 |  | 
REGISTER FILE CONTENTS | 
MAR | ?/0xE10/0xC84/0xE14/0xC88/0xC84
MDR | ?/6/10/6/16
PC | 0x18/0x19/0x1A/0x1B/0x1C/0x1D/0x1E
MBR | 0x15/0x00/0x15/0x01/0x60/0x36/0x02
SP | 0xC80/0xC84/0xC88/0xC84
TOS | ?/6/10/16
LV | 0xE10
H | ?/0xE10/0xE10/10/0xE10

## Slide 72
19. istore2: MAR = MBRU + H
 |  |  | 0x18 | 0x15 | 
0xC80 |  |  | 0x19 | 0x00 | 
0xC84 | 16 |  SP | 0x1A | 0x15 | 
0xC88 | 10 |  | 0x1B | 0x01 | 
 |  |  | 0x1C | 0x60 | 
 |  |  | 0x1D | 0x36 | 
 |  |  | 0x1E | 0x02 |  PC
 |  |  | 0x1F |  | 
 |  |  | 0x20 |  | 
0xE10 | a: 6 |  LV | 0x21 |  | 
0xE14 | b: 10 |  | 0x22 |  | 
0xE18 | c: 8 |  | 0x23 |  | 
 |  |  | 0x24 |  | 
 |  |  | 0x25 |  | 
 |  |  | 0x26 |  | 
REGISTER FILE CONTENTS | 
MAR | ?/0xE10/0xC84/0xE14/0xC88/0xC84/0xE18
MDR | ?/6/10/6/16
PC | 0x18/0x19/0x1A/0x1B/0x1C/0x1D/0x1E
MBR | 0x15/0x00/0x15/0x01/0x60/0x36/0x02
SP | 0xC80/0xC84/0xC88/0xC84
TOS | ?/6/10/16
LV | 0xE10
H | ?/0xE10/0xE10/10/0xE10

## Slide 73
20. istore3: MDR = TOS; wr
 |  |  | 0x18 | 0x15 | 
0xC80 |  |  | 0x19 | 0x00 | 
0xC84 | 16 |  SP | 0x1A | 0x15 | 
0xC88 | 10 |  | 0x1B | 0x01 | 
 |  |  | 0x1C | 0x60 | 
 |  |  | 0x1D | 0x36 | 
 |  |  | 0x1E | 0x02 |  PC
 |  |  | 0x1F |  | 
 |  |  | 0x20 |  | 
0xE10 | a: 6 |  LV | 0x21 |  | 
0xE14 | b: 10 |  | 0x22 |  | 
0xE18 | c: 8 |  | 0x23 |  | 
 |  |  | 0x24 |  | 
 |  |  | 0x25 |  | 
 |  |  | 0x26 |  | 
REGISTER FILE CONTENTS | 
MAR | ?/0xE10/0xC84/0xE14/0xC88/0xC84/0xE18
MDR | ?/6/10/6/16/16
PC | 0x18/0x19/0x1A/0x1B/0x1C/0x1D/0x1E
MBR | 0x15/0x00/0x15/0x01/0x60/0x36/0x02
SP | 0xC80/0xC84/0xC88/0xC84
TOS | ?/6/10/16
LV | 0xE10
H | ?/0xE10/0xE10/10/0xE10

## Slide 74
21. istore4: SP = MAR = SP – 1; rd
 |  |  | 0x18 | 0x15 | 
0xC80 |  |  SP | 0x19 | 0x00 | 
0xC84 | 16 |  | 0x1A | 0x15 | 
0xC88 | 10 |  | 0x1B | 0x01 | 
 |  |  | 0x1C | 0x60 | 
 |  |  | 0x1D | 0x36 | 
 |  |  | 0x1E | 0x02 |  PC
 |  |  | 0x1F |  | 
 |  |  | 0x20 |  | 
0xE10 | a: 6 |  LV | 0x21 |  | 
0xE14 | b: 10 |  | 0x22 |  | 
0xE18 | c: 8/16 |  | 0x23 |  | 
 |  |  | 0x24 |  | 
 |  |  | 0x25 |  | 
 |  |  | 0x26 |  | 
REGISTER FILE CONTENTS | 
MAR | ?/0xE10/0xC84/0xE14/0xC88/0xC84/0xE18/0xC80
MDR | ?/6/10/6/16/16
PC | 0x18/0x19/0x1A/0x1B/0x1C/0x1D/0x1E
MBR | 0x15/0x00/0x15/0x01/0x60/0x36/0x02
SP | 0xC80/0xC84/0xC88/0xC84/0x80
TOS | ?/6/10/16
LV | 0xE10
H | ?/0xE10/0xE10/10/0xE10

## Slide 75
22. istore5: PC = PC + 1; fetch
 |  |  | 0x18 | 0x15 | 
0xC80 |  |  SP | 0x19 | 0x00 | 
0xC84 | 16 |  | 0x1A | 0x15 | 
0xC88 | 10 |  | 0x1B | 0x01 | 
 |  |  | 0x1C | 0x60 | 
 |  |  | 0x1D | 0x36 | 
 |  |  | 0x1E | 0x02 | 
 |  |  | 0x1F |  |  PC
 |  |  | 0x20 |  | 
0xE10 | a: 6 |  LV | 0x21 |  | 
0xE14 | b: 10 |  | 0x22 |  | 
0xE18 | c: 8/16 |  | 0x23 |  | 
 |  |  | 0x24 |  | 
 |  |  | 0x25 |  | 
 |  |  | 0x26 |  | 
REGISTER FILE CONTENTS | 
MAR | ?/0xE10/0xC84/0xE14/0xC88/0xC84/0xE18/0xC80
MDR | ?/6/10/6/16/16/?
PC | 0x18/0x19/0x1A/0x1B/0x1C/0x1D/0x1E/0x1F
MBR | 0x15/0x00/0x15/0x01/0x60/0x36/0x02
SP | 0xC80/0xC84/0xC88/0xC84/0x80
TOS | ?/6/10/16
LV | 0xE10
H | ?/0xE10/0xE10/10/0xE10

## Slide 76
23. istore6: TOS = MDR; goto Main1... DONE!
 |  |  | 0x18 | 0x15 | 
0xC80 |  |  SP | 0x19 | 0x00 | 
0xC84 | 16 |  | 0x1A | 0x15 | 
0xC88 | 10 |  | 0x1B | 0x01 | 
 |  |  | 0x1C | 0x60 | 
 |  |  | 0x1D | 0x36 | 
 |  |  | 0x1E | 0x02 | 
 |  |  | 0x1F |  |  PC
 |  |  | 0x20 |  | 
0xE10 | a: 6 |  LV | 0x21 |  | 
0xE14 | b: 10 |  | 0x22 |  | 
0xE18 | c: 8/16 |  | 0x23 |  | 
 |  |  | 0x24 |  | 
 |  |  | 0x25 |  | 
 |  |  | 0x26 |  | 
REGISTER FILE CONTENTS | 
MAR | ?/0xE10/0xC84/0xE14/0xC88/0xC84/0xE18/0xC80
MDR | ?/6/10/6/16/16/?
PC | 0x18/0x19/0x1A/0x1B/0x1C/0x1D/0x1E/0x1F
MBR | 0x15/0x00/0x15/0x01/0x60/0x36/0x02
SP | 0xC80/0xC84/0xC88/0xC84/0x80
TOS | ?/6/10/16
LV | 0xE10
H | ?/0xE10/0xE10/10/0xE10

## Slide 77: 4. Show changing contents of the data cell.
 |  |  | 0x18 | 0x15 | 
0xC80 |  |  SP | 0x19 | 0x00 | 
0xC84 | 16 |  | 0x1A | 0x15 | 
0xC88 | 10 |  | 0x1B | 0x01 | 
 |  |  | 0x1C | 0x60 | 
 |  |  | 0x1D | 0x36 | 
 |  |  | 0x1E | 0x02 | 
 |  |  | 0x1F |  |  PC
 |  |  | 0x20 |  | 
0xE10 | a: 6 |  LV | 0x21 |  | 
0xE14 | b: 10 |  | 0x22 |  | 
0xE18 | c: 8/16 |  | 0x23 |  | 
 |  |  | 0x24 |  | 
 |  |  | 0x25 |  | 
 |  |  | 0x26 |  | 
REGISTER FILE CONTENTS | 
MAR | ?/0xE10/0xC84/0xE14/0xC88/0xC84/0xE18/0xC80
MDR | ?/6/10/6/16/16/?
PC | 0x18/0x19/0x1A/0x1B/0x1C/0x1D/0x1E/0x1F
MBR | 0x15/0x00/0x15/0x01/0x60/0x36/0x02
SP | 0xC80/0xC84/0xC88/0xC84/0x80
TOS | ?/6/10/16
LV | 0xE10
H | ?/0xE10/0xE10/10/0xE10

## Slide 78: Design Optimizations
The MIC-1 works, but what we want to do is improve on the existing design to optimize the design metrics of a system. Those of which include:
speed
cost
size
power consumption
These will often have trade-offs! We will focus on speed and cost here.

## Slide 79: Speed vs. Cost
Given a circuit technology and an ISA, we have two main methods of gaining speed:
Hardware: speeding up through new hardware
Organization: speeding up by reorganizing. There are three ways.
  reducing the number of clock cycles needed to execute an instruction
  simplify organization so clock cycle can be shorter
  overlap execution of instructions
These come with their own costs (e.g. complex and faster means $$). Similar to a memory hierarchy, we can use a small amount of fast parts.

## Slide 80: Reducing Execution Path Length
To reduce the number of micro-instructions per ISA instruction, we could do the following to our MIC-1 Processor to make it a MIC-2 Processor:
merge the interpreter loop with microcode
  Main1 is called in every instruction, so we can merge the instructions of Main1 into each one
  trade-off: some instructions could be made longer!
add another bus
  H is the only register that can be used in the ALU with the B-Bus in Mic-1, so we can add the A-Bus to allow all registers to be an input for ALU
  trade-off: bigger bus = bigger microinstructions = bigger control store
add an instruction fetch unit
  PC has to be incremented (using the ALU) and the next instruction is fetched every instruction, so we make a unit that pre-fetches the bytes and independently increments PC
  trade-off: a new unit is made, taking up space and costing more

## Slide 81: Splitting the Datapath
Recall that for our clock cycle in MIC-1, we had to wait for signals to propagate through the whole datapath, i.e. our Registers, A-Bus, and B-Bus + ALU + C-Bus. We can break our datapath into these three steps by adding latches/flip-flops to break each part!
We can now speed up the clock by decreasing the minimum delay and giving access to all parts of the datapath during a cycle.
This splits the 1 microinstruction into 3 steps:
A-Bus and B-Bus = Registers
C-Bus = ALU Result
Registers = C-Bus; Memory Operations

## Slide 82: Pipelining
By splitting up the datapath, we have allowed the processor to run each part of the datapath cycle in conjunction with each other! Along with the pre-fetched instructions from MIC-2, adding registers to split the datapath means we can make the MIC-3 processor.
Every cycle, we will try to issue a new microinstruction, making the total amount of time for a pipelined instruction to be smaller than or equal (never greater) than an un-pipelined instruction.
There are cases in which some microinstructions depend on the results of other microinstructions – this is called Read-After-Write Dependence and happens when a write is initiated but MDR is needed in another microinstruction before the write completes, so that microinstruction has to wait until the write finishes before reading.

## Slide 83: Example MIC-3 Simulation
For the following IJVM instruction, show the pipelined sequences and stages:
ILOAD a

## Slide 84
For pipelining, since we’re now using the MIC-3 (and thus MIC-2) microprogram, we can focus on these microinstructions for our pipeline sequence.
Label | Operations
iload1 | MAR = LV + MBR1U; rd
iload2 | MAR = SP = SP + 1
iload3 | TOS = MDR; wr; goto MBR1
Note:
read – MDR = MEM[MAR]32
write – MEM[MAR]32 = MDR

## Slide 85
Here is the order of the microinstructions based on our IJVM instructions:
iload1
iload2
iload3
ILOAD a

## Slide 86
1. iload1: MAR = LV + MBR1U; rd
Cycle | iload1
1 | A = LV; B = MBR1U
2 | C = A + B;
3 | MAR = C; rd
4 | MDR = MEM

## Slide 87
2. iload2: MAR = SP = SP + 1
Cycle | iload1 | iload2
1 | A = LV; B = MBR1U | 
2 | C = A + B; | B = SP
3 | MAR = C; rd | C = B + 1;
4 | MDR = MEM | MAR = SP = C

## Slide 88
Cycle | iload1 | iload2 | iload3
1 | A = LV; B = MBR1U |  | 
2 | C = A + B; | B = SP | 
3 | MAR = C; rd | C = B + 1; | 
4 | MDR = MEM | MAR = SP = C | 
5 |  |  | B = MDR
6 |  |  | C = B
7 |  |  | TOS = C; wr
8 |  |  | MEM = MDR
3. iload3: TOS = MDR; wr; goto MBR1... DONE!
Notice the RAW
Dependency here

## Slide 89: Improving Performance
We can also work on improving the memory of the processor to make the system better. Main memory itself is big but slow, which means the CPU could be waiting for a while even if its fast. Processors put a lot of demands on a memory system in terms of
latency – the delay in supplying an operand
bandwidth – the amount of data supplied per unit of time
We can fix this dynamic by adding extra memory on the processor, which would be a cache.

## Slide 90: Cache Properties
inclusive – lower-level/smaller caches are fully contained in higher-level/bigger caches
predictive – brings in data to memory based on
  temporal locality (a location may be accessed soon)
    determines what gets flushed and written; least-recently-used cache line
  spatial locality (neighboring locations may be accessed soon)
    determines block size
associativity – how many places a piece of data can go
  depends on type of cache
hit/misses – whether an address can be used from cache
  is a hit if address is found in the cache AND valid is on

## Slide 91: Types of Caches
Fully Associative – any location in memory –> any location in cache
  slow and costly
Direct Mapped – any location in memory –> one location in cache
  fast, but risk lots of overwriting
k-way Set Associative – any location in memory –> any location in set
Note: to find an address in a cache, the address is compared to every block in the cache. This is expensive and slow, especially with a fully-associative cache.

## Slide 92: Addresses for Caches
For a cache with n-byte blocks, the 8-bit address will be partitioned based on the type of cache as well as the size of the blocks:
offset = log2n bits – describes the offset in the cache line
associativity = log2(# of entries) bits – describes where to look for the hits
tag = dependent – the part of the address that is searched
tag (8 – offset) | offset (log2n bits)
tag (8 – cache line – offset) | cache line (log2m bits) | offset (log2n bits)
tag (8 – set– offset) | set (log2m/k bits) | offset (log2n bits)
For an 8-bit address, this is how the address is partitioned:
fully associative
direct mapped
k-way associative